## Slide 1: Design of Digital Circuits Lecture 17a: Superscalar Execution
Prof. Onur Mutlu
ETH Zurich
Spring 2019
18 April 2019

## Slide 2: Required Readings
This week
  Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proceedings of the IEEE, 1995
  H&H Chapters 7.8 and 7.9
  McFarling, “Combining Branch Predictors,” DEC WRL Technical Report, 1993.

## Slide 3: Agenda for Today & Next Few Lectures
Single-cycle Microarchitectures
Multi-cycle and Microprogrammed Microarchitectures
Pipelining
Issues in Pipelining: Control & Data Dependence Handling, State Maintenance and Recovery, …
Out-of-Order Execution
Other Execution Paradigms

## Slide 4: Recall: OOO Execution: Restricted Dataflow
An out-of-order engine dynamically builds the dataflow graph of a piece of the program
  which piece?
The dataflow graph is limited to the instruction window
  Instruction window: all decoded but not yet retired instructions
Can we do it for the whole program?
Why would we like to?
In other words, how can we have a large instruction window?
Can we do it efficiently with Tomasulo’s algorithm?

## Slide 5: Recall: State of RAT and RS in Cycle 7
+
∗
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 0 | a | 
R6 | 1 |  | 6
R7 | 0 | b | 
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 0 | x |  | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d |  |  |  |  |  | 
0
a
0
y
0
d
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 0 | b |  | 0 | c | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 

## Slide 6: Recall: Dataflow Graph

## Slide 7: Other Approaches to Concurrency (or Instruction Level Parallelism)

## Slide 8: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 9: Review: Data Flow: Exploiting Irregular Parallelism

## Slide 10: Data Flow Summary
Availability of data determines order of execution
A data flow node fires when its sources are ready
Programs represented as data flow graphs (of nodes)
Data Flow at the ISA level has not been (as) successful
Data Flow implementations at the microarchitecture level (while preserving Von Neumann semantics) have been very successful
  Out of order execution is the prime example

## Slide 11: Pure Data Flow Advantages/Disadvantages
Advantages
  Very good at exploiting irregular parallelism
  Only real dependencies constrain processing
  More parallelism can be exposed than Von Neumann model
Disadvantages
  No precise state semantics
    Debugging very difficult
    Interrupt/exception handling is difficult (what is precise state semantics?)
  Too much parallelism? (Parallelism control needed)
  High bookkeeping overhead (tag matching, data storage)
  …

## Slide 12: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 13: Superscalar Execution

## Slide 14: Superscalar Execution
Idea: Fetch, decode, execute, retire multiple instructions per cycle
  N-wide superscalar  N instructions per cycle
Need to add the hardware resources for doing so
Hardware performs the dependence checking between concurrently-fetched instructions
Superscalar execution and out-of-order execution are orthogonal concepts
  Can have all four combinations of processors:
    [in-order, out-of-order] x [scalar, superscalar]

## Slide 15: In-Order Superscalar Processor Example
Multiple copies of datapath: Can fetch/decode/execute multiple instructions per cycle
Dependencies make it tricky to issue multiple instructions at once
Here: Ideal IPC = 2

## Slide 16: In-Order Superscalar Performance Example
lw $t0, 40($s0)
add $t1, $s1, $s2
sub $t2, $s1, $s3 and $t3, $s3, $s4 or $t4, $s1, $s5
sw $s5, 80($s0)
Ideal IPC = 2
Actual IPC = 2 (6 instructions issued in 3 cycles)

## Slide 17: Superscalar Performance with Dependencies
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 and $t2, $s4, $t0 or $t3, $s5, $s6
sw $s7, 80($t3)
Ideal IPC = 2
Actual IPC = 1.2 (6 instructions issued in 5 cycles)

## Slide 18: Superscalar Execution Tradeoffs
Advantages
  Higher IPC (instructions per cycle)
Disadvantages
  Higher complexity for dependency checking
    Require checking within a pipeline stage
    Renaming becomes more complex in an OoO processor
  More hardware resources needed

## Slide 19: Design of Digital Circuits Lecture 17a: Superscalar Execution
Prof. Onur Mutlu
ETH Zurich
Spring 2019
18 April 2019

## Slide 20: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 21: VLIW

## Slide 22: VLIW Concept
Superscalar
  Hardware fetches multiple instructions and checks dependencies between them
VLIW (Very Long Instruction Word)
  Software (compiler) packs independent instructions in a larger “instruction bundle” to be fetched and executed concurrently
  Hardware fetches and executes the instructions in the bundle concurrently
No need for hardware dependency checking between concurrently-fetched instructions in the VLIW model

## Slide 23: VLIW Concept
Fisher, “Very Long Instruction Word architectures and the ELI-512,” ISCA 1983.
  ELI: Enormously longword instructions (512 bits)

## Slide 24: VLIW (Very Long Instruction Word)
A very long instruction word consists of multiple independent instructions packed together by the compiler
  Packed instructions can be logically unrelated (contrast with SIMD/vector processors, which we will see soon)
Idea: Compiler finds independent instructions and statically schedules (i.e. packs/bundles) them into a single VLIW instruction
Traditional Characteristics
  Multiple functional units
  All instructions in a bundle are executed in lock step
  Instructions in a bundle statically aligned to be directly fed into the functional units

## Slide 25: VLIW Performance Example (2-wide bundles)
lw $t0, 40($s0)
add $t1, $s1, $s2
sub $t2, $s1, $s3 and $t3, $s3, $s4 or $t4, $s1, $s5
sw $s5, 80($s0)
Ideal IPC = 2
Actual IPC = 2 (6 instructions issued in 3 cycles)

## Slide 26: VLIW Lock-Step Execution
Lock-step (all or none) execution: If any operation in a VLIW instruction stalls, all instructions stall
In a truly VLIW machine, the compiler handles all dependency-related stalls, hardware does not perform dependency checking
  What about variable latency operations?

## Slide 27: VLIW Philosophy
Philosophy similar to RISC (simple instructions and hardware)
  Except multiple instructions in parallel
RISC (John Cocke, 1970s, IBM 801 minicomputer)
  Compiler does the hard work to translate high-level language code to simple instructions (John Cocke: control signals)
    And, to reorder simple instructions for high performance
  Hardware does little translation/decoding  very simple
VLIW (Josh Fisher, ISCA 1983)
  Compiler does the hard work to find instruction level parallelism
  Hardware stays as simple and streamlined as possible
    Executes each instruction in a bundle in lock step
    Simple  higher frequency, easier to design

## Slide 28: Commercial VLIW Machines
Multiflow TRACE, Josh Fisher (7-wide, 28-wide)
Cydrome Cydra 5, Bob Rau
Transmeta Crusoe: x86 binary-translated into internal VLIW
TI C6000, Trimedia, STMicro (DSP & embedded processors)
  Most successful commercially
Intel IA-64
  Not fully VLIW, but based on VLIW principles
  EPIC (Explicitly Parallel Instruction Computing)
  Instruction bundles can have dependent instructions
  A few bits in the instruction format specify explicitly which instructions in the bundle are dependent on which other ones

## Slide 29: VLIW Tradeoffs
Advantages
  + No need for dynamic scheduling hardware  simple hardware
  + No need for dependency checking within a VLIW instruction  simple hardware for multiple instruction issue + no renaming
  + No need for instruction alignment/distribution after fetch to different functional units  simple hardware
Disadvantages
  -- Compiler needs to find N independent operations per cycle
  -- If it cannot, inserts NOPs in a VLIW instruction
  -- Parallelism loss AND code size increase
  -- Recompilation required when execution width (N), instruction latencies, functional units change (Unlike superscalar processing)
  -- Lockstep execution causes independent operations to stall
  -- No instruction can progress until the longest-latency instruction completes

## Slide 30: VLIW Summary
VLIW simplifies hardware, but requires complex compiler techniques
Solely-compiler approach of VLIW has several downsides that reduce performance
  -- Too many NOPs (not enough parallelism discovered)
  -- Static schedule intimately tied to microarchitecture
  -- Code optimized for one generation performs poorly for next
  -- No tolerance for variable or long-latency operations (lock step)
++ Most compiler optimizations developed for VLIW employed in optimizing compilers (for superscalar compilation)
  Enable code optimizations
++ VLIW successful when parallelism is easier to find by the compiler (traditionally embedded markets, DSPs)

## Slide 31: An Example Work: Superblock
Lecture Video on Static Instruction Scheduling
  https://www.youtube.com/watch?v=isBEVkIjgGA
Hwu et al., The superblock: An effective technique for VLIW and superscalar compilation.
The Journal of Supercomputing, 1993.

## Slide 32: Another Example Work: IMPACT
Chang et al., IMPACT: an architectural framework for multiple-instruction-issue processors. ISCA 1991.

## Slide 33: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 34: Recall: How to Handle Data Dependences
Anti and output dependences are easier to handle
  write to the destination in one stage and in program order
Flow dependences are more interesting
Five fundamental ways of handling flow dependences
  Detect and wait until value is available in register file
  Detect and forward/bypass data to dependent instruction
  Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Predict the needed value(s), execute “speculatively”, and verify
  Do something else (fine-grained multithreading)
    No need to detect

## Slide 35: How to Handle Control Dependences
Critical to keep the pipeline full with correct sequence of dynamic instructions.
Potential solutions if the instruction is a control-flow instruction:
Stall the pipeline until we know the next fetch address
Guess the next fetch address (branch prediction)
Employ delayed branching (branch delay slot)
Do something else (fine-grained multithreading)
Eliminate control-flow instructions (predicated execution)
Fetch from both possible paths (if you know the addresses of both possible paths) (multipath execution)

## Slide 36: Fine-Grained Multithreading

## Slide 37: Fine-Grained Multithreading
Idea: Hardware has multiple thread contexts (PC+registers). Each cycle, fetch engine fetches from a different thread.
  By the time the fetched branch/instruction resolves, no instruction is fetched from the same thread
  Branch/instruction resolution latency overlapped with execution of other threads’ instructions
+ No logic needed for handling control and
data dependences within a thread
-- Single thread performance suffers
-- Extra logic for keeping thread contexts
-- Does not overlap latency if not enough
threads to cover the whole pipeline
Notes: Latency overlap/hiding

## Slide 38: Fine-Grained Multithreading (II)
Idea: Switch to another thread every cycle such that no two instructions from a thread are in the pipeline concurrently
Tolerates the control and data dependency latencies by overlapping the latency with useful work from other threads
Improves pipeline utilization by taking advantage of multiple threads
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.

## Slide 39: Fine-Grained Multithreading: History
CDC 6600’s peripheral processing unit is fine-grained multithreaded
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Processor executes a different I/O thread every cycle
  An operation from the same thread is executed every 10 cycles
Denelcor HEP (Heterogeneous Element Processor)
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.
  120 threads/processor
  available queue vs. unavailable (waiting) queue for threads
  each thread can have only 1 instruction in the processor pipeline; each thread independent
  to each thread, processor looks like a non-pipelined machine
  system throughput vs. single thread performance tradeoff

## Slide 40: Fine-Grained Multithreading in HEP
Cycle time: 100ns
8 stages  800 ns to complete an instruction
  assuming no memory access
No control and data dependency checking
Burton Smith
(1941-2018)

## Slide 41: Multithreaded Pipeline Example
Slide credit: Joel Emer

## Slide 42: Sun Niagara Multithreaded Pipeline
Kongetira et al., “Niagara: A 32-Way Multithreaded Sparc Processor,” IEEE Micro 2005.

## Slide 43: Fine-grained Multithreading
Advantages
  + No need for dependency checking between instructions
  (only one instruction in pipeline from a single thread)
  + No need for branch prediction logic
  + Otherwise-bubble cycles used for executing useful instructions from different threads
  + Improved system throughput, latency tolerance, utilization
Disadvantages
  - Extra hardware complexity: multiple hardware contexts (PCs, register files, …), thread selection logic
  - Reduced single thread performance (one instruction fetched every N cycles from the same thread)
  - Resource contention between threads in caches and memory
  - Some dependency checking logic between threads remains (load/store)

## Slide 44: Modern GPUs are FGMT Machines

## Slide 45: NVIDIA GeForce GTX 285 “core”
…
= instruction stream decode
= data-parallel (SIMD) func. unit,
control shared across 8 units
= execution context storage
= multiply-add
= multiply
64 KB of storage
for thread contexts (registers)
Slide credit: Kayvon Fatahalian
Notes: 30 * 32 * 32 = 30 * 1024 = 30K fragments
64KB register file = 16 32-bit registers per thread = 64B (1/32 that of LRB)
16KB of shared scratch
80KB / core available to software

## Slide 46: NVIDIA GeForce GTX 285 “core”
…
64 KB of storage
for thread contexts (registers)
Groups of 32 threads share instruction stream (each group is a Warp): they execute the same instruction on different data
Up to 32 warps are interleaved in an FGMT manner
Up to 1024 thread contexts can be stored
Slide credit: Kayvon Fatahalian
Notes: To get maximal latency hiding:
Run 1/32 of the time
16 words per thread = 64B

## Slide 47: NVIDIA GeForce GTX 285
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
30 cores on the GTX 285: 30,720 threads
Slide credit: Kayvon Fatahalian
Notes: If you’re running a CUDA program, and your not launching 30K threads, you are certainly not getting full latency hiding, and you might not be using the GPU well

## Slide 48: End of Fine-Grained Multithreading